## Slide 1: EN.525.726 – Applications of Power Electronics Design Project Milestone 6
Hoang Nguyen
05/05/24

## Slide 2: Main Requirements
Topology: Flyback Converter
Vin: 12V
Vout: 5V
Load Current Range: 0-5A
Output Ripple: +/- 0.1V (steady-state), +/- 0.2V during load step from 3A to 5A and 5A to 3A
Efficiency: >75% at full-load
PCB: 2 layers
PCB dimension: < 10 in^2

## Slide 3: Power Stage Design (1)
Switching Frequency = 200 Khz
Transformer’s turn’s ratio = 1
Operate in both DCM and CCM
Peak-peak Flyback transformer primary current ripple = 40% of max magnetizing inductance current

## Slide 4: Power Stage Design (2)
Inductance
Output voltage ripple = 0.1V
Transient Voltage Requirement = 0.2 V during 3A to 5A load step
The crossover frequency , Assume

## Slide 5: Controller Design (1) – Type III compensator
CCM_full load
DCM_ no load

## Slide 6: Controller Design (2)

## Slide 7: Schematic
Power Stage
Controller

## Slide 8: PCB Layout

## Slide 9: Transformer Design (1)
Turn’s ratio = 1
Allowed copper loss = 3% of 25W
250mT
Select the PQ Core, type PQ20/16 with
Choose 22AWG Wire for both primary and secondary turns so that they are next to each other and fit the bobbin width.

## Slide 10: Transformer Design (2)
Primary winding:
  clockwise for 4 turns
  Start from bottom end at the top of bobbin
Secondary winding:
  Start from the other window
  clockwise so that the 1st turn of the secondary copper is next to the 1st turn of the primary copper and so on
  Start from bottom end at the top of bobbin
Add 1 layer of Kapton tape at the center of the core then measure the inductance
Repeat until the measured inductance matched with desired value.

## Slide 11: Transformer Design (3)
Measured inductance: 6.6uH
Desired Inductance: 6.3uH

## Slide 12: Circuit Board Assembly (top)

## Slide 13: Circuit Board Assembly (bottom)

## Slide 14: Turn on Waveform – No Load

## Slide 15: Turn on Waveform – 5A Load

## Slide 16: Efficiency vs Load Current
Chart: Efficiency vs Load Current
| 0.99199999999999999 | 1.9239999999999999 | 2.8330000000000002 | 3.6779999999999999 | 4.5
Measured Eff | 75.2142 | 78.726 | 79.4211 | 78.9847 | 78.323

## Slide 17: Steady state – No load

## Slide 18: Steady state – 5A load

## Slide 19: Load Step Response (1)

## Slide 20: Load Step Response (2)

## Slide 21: Load Step Response (3)

## Slide 22: Load Step Response (4)

## Slide 23: Learning that will be applied for future designs
Design compensator
Using average model for simulation
Calculate and build a custom transformer/inductor
Kicad